# ITCM 410:	Construction Surveying		Instructor:	Joe Curd, Jr.

Test 1/Answers					Name:

February 10, 2011

Leveling (2 Pts. Each)

(1a)	What does the term elevation mean?

Elevation is vertical distance above or below datum.

(1b)	What is the purpose of running levels?

Determine elevation of features.

(1c)	What is the purpose of waving the rod?  Which rod reading should be recorded – the highest or lowest?

Accuracy/Lowest

(1d)	What is the purpose of equalizing BS and FS distance?

+/- Sights to transfer elevations

(1e)	What is meant by level circuit and arithmetic check?

Loop/Closure for accuracy

(2)	Convert the following: (5 Pts. Each)

DMS			        D.D.

22° 37’ 48”			        22.63

57-19-12   			      57.32°

173° 18’ 22”			     173.306

63-59-24       		     	       63.99°

(3)	Given the following survey point coordinates, find the bearing and distance from point 1 - 2. (10 Pts. Each)

N				         E

(a)	1	10000.0000			10000.0000

2	10000.8924			10000.4467

S 26-35-27 E

0.9980’

(b)	1	  5000.0000			  5000.0000

2	  5732.8500			  5142.3280

N 10-59-24 E

746.543

(4)	If the perimeter of a traverse is 35,452 feet, what is the relative error of closure for 3a (above) coordinates if they represent the ending and beginning points? (5 Pts.)

1:35,523

(5)	Determine the bearing and distance between traverse points and determine from the coordinates the area in acres.  (20 Pts.)

N			     E

(1)	5000.00		5000.00		N 4-0-1 E    		250.00

(2)	5249.39		5017.44		S 78-28-52 W		520.00

(3)	5145.55		4507.91		S 14-59-55 W		452.33

(4)	4708.63		4624.98		S 84-0-03 W		350.01

(5)	4672.05		4973.07		N 4-4-39 E		329.05

(1)	5000.00		5000.00			     5.03 Acres

(6)	Determine latitude and departures, error of closure, adjusted bearings and distance by compass rule and area in acres of the following traverse data. (25 Pts.)

(1)	N 22° 15 E		  750.25’

(2)	S 80° 30 W		  962.58’

(3)	S 10° 15 E		  732.52’

(4)	S 35° 30 W		  872.45’

- S 80° 13 W		  915.23’

- S 82° 10 W		  113.25’

- N 50° 15 W		  700.13’

- N 66° 20 E		1242.45’

- N 85° 16 E 		1462.11’

## UNADJUSTED

1						5000.0000	5000.0000

N 22-15 E	750.25

2						5694.3868	5284.0811

S 80-30 W  	962.58

3						5535.5152	4334.7023

S 10-15 E	732.52

4						4814.6857	4465.0495

S 35-30 W	872.45

5						4104.4107	3958.4152

S 80-13 W	915.23

6						3948.8922	3056.4951

S 82-10 W	113.25

7						3933.4571	2944.3091

N 50-15 W	700.13

8						4381.1475	2406.0126

N 66-20 E	1242.45

9						4879.8856	3543.9680

N 85-16 E	1462.11

10						5000.5365	5001.0915

1

Error of Closure	=	1.2169’

Precision 	=	1:6373

## ADJUSTED

1						5000.0000	5000.0000

N 22-14-39 E		750.16

2						5694.3349	5283.9754

S 80-29-51 W		962.72

3						5535.3967	4334.4611

S 10-14-29 E		732.55

4						4814.5165	4464.7052

S 35-30-15 W		872.57

5						4104.1810	3957.9480

S 80-12-51 W		915.37

6						3948.5992	3055.8990

S 82-09-50 W		113.27

7						3933.1563	2943.6898

N 50-15-30 W		200.17

8						4380.7983	2405.3020

N 66-20-01 E		1242.26

9						4879.4503	3543.0824

N 85-16-12 E		1461.90

10						5000.0000	5000.0000

Acreage = 17.30571