Lab Report 2

Kelsey Bradley

May 12, 2011

OBJECTIVE

The objectives in this lab were to go around Lloyd Cassidy and locate all of the corners and doors with a theodolite and a total station. This was to teach us how to better use the equipment that we will need for surveying.

PROCEDURE

To begin this lab, we were to use a total station to measure the distances from the total station to the corners of the building. We also had to measure the angles and distances from the doors too. This was the easiest way to do this. When we had to do it with the theodolite, we couldn't use the prism poles to measure the angles easily. It had to be done with the philadelphia rod, which made it considerably harder.

FINDINGS

|  | Unadjusted |  |
| --- | --- | --- |
|  | Bearings | Distance | Latitude | Departure |
| 1 |  |  |  |  |
|  | S 75⁰ E | 178.100' | -46.096 | 172.031 |
| 2 |  |  |  |  |
|  | N 36⁰ 33' 10" E | 178.023' | 143.007 | 106.024 |
| 7 |  |  |  |  |
|  | N 4⁰ 33' 10" E | 63.690' | 63.489 | 5.056 |
| 12 |  |  |  |  |
|  | N 54⁰ 26' 50" W | 130.000' | 75.589 | -105.765 |
| 13 |  |  |  |  |
|  | S 41⁰ 05' W | 103.550' | -78.051 | -68.049 |
| 15 |  |  |  |  |
|  | S 40⁰ 05' W | 102.760' | -78.623 | -66.167 |
| 17 |  |  |  |  |
|  | S 28⁰ 28' 16" W | 90.273' | -79.355 | -43.035 |
| 1 |  |  |  |  |
|  |  | Per: 846.396 | Σ lat: -0.04 | Σ dep: 0.095 |

| Compass Rule Adjustments |
| --- |
|  | Latitude | Departure |
| 1 | 0.00842 | -0.01999 |
| 2 | 0.00841 | -0.01998 |
| 7 | 0.00301 | -0.00715 |
| 12 | 0.00614 | -0.01459 |
| 13 | 0.00489 | -0.01162 |
| 15 | 0.00486 | -0.01153 |
| 17 | 0.00427 | -0.01013 |

|  |  |  | Adjusted |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Bearings | Distance | Latitude | Departure | Northing | Easting |
| 1 |  |  |  |  | 5000 | 5000 |
|  | S 75⁰ E | 178.069' | -46.08758 | 172.01101 |  |  |
| 2 |  |  |  |  | 4953.91242 | 5172.01101 |
|  | N 36⁰ 33' 10" E | 178.033' | 143.01541 | 106.00402 |  |  |
| 7 |  |  |  |  | 5096.92783 | 5278.01503 |
|  | N 4⁰ 33' 10" E | 63.693' | 63.49201 | 5.04885 |  |  |
| 12 |  |  |  |  | 5160.41984 | 5283.06388 |
|  | N 54⁰ 26' 50" W | 130.011' | 75.59514 | -105.77959 |  |  |
| 13 |  |  |  |  | 5236.01498 | 5177.28429 |
|  | S 41⁰ 05' W | 103.543' | -78.04611 | -68.06062 |  |  |
| 15 |  |  |  |  | 5157.96887 | 5109.22367 |
|  | S 40⁰ 05' W | 102.754' | -78.61814 | -66.17853 |  |  |
| 17 |  |  |  |  | 5079.35073 | 5043.04514 |
|  | S 28⁰ 28' 16" W | 90.268' | -79.35073 | -43.04514 |  |  |
| 1 |  |  | 0 | 0 | 5000 | 5000 |

Error of Closure

0.103077641

846.396/0.103077641

1: 8,300

| Total Area in Acres |
| --- |
| N: | 183811830.3 |
| E: | 183722696.4 |
| Diff: | 89133.4 |
| Acres: | 1.02 |

CONCLUSION

In conclusion this lab wasn’t that bad. I felt like I learned a lot in this lab. I now know how to better use Carlson software. I also know how to use a total station and a prism pole now. It was beneficial to me to learn all of this stuff.